## Slide 1
AMR
Parts manufacturing

## Slide 2
P0015 | 135deg_small_braket M6 3holes
Units: 4 + 4
Assembly: Chassis Top, Chassis Bottom
Source model: “Aluminum 30mm x 3mm flat bar” / 135degree_small_braket v2.FCStd

## Slide 3
Length: 210mm, diameter: 16mm, wall: 0,5mm
Cut angle: 90deg both sides
Units: 1
Assembly: Clutch set
P0430 | Clutch axel (tube 410x16mm)
P0435 | Balancing axel (tube 390x16mm)
Length: 210mm, diameter: 16mm, wall: 0,5mm
Cut angle: 90deg both sides
Units: 1
Assembly: Balancing axel set
P0390 | Clutch lever (100x5mm bar)
Length: 100mm, diameter: 5mm
Cut angle: 90deg both sides
Units: 1
Assembly: Clutch set

## Slide 4
P0160 | 30x30 204mm profile 22,5deg cut
P0165 | 30x30 138mm profile 22,5deg cut
P0155 | 30x30 339 mm profile flat cut
Units: 2 + 2
Assembly: Chassis Top, Chassis Bottom
P0170 | 30x30_200mm profile flat cut
P0175 | 30x30_60mm profile flat cut
Units: 4
Assembly: Chassis Middle
Units: 2
Assembly: Set limit motors Top
Length long side: 204mm
Cut angle: 22,5deg both sides
Units: 4 + 4
Assembly: Chassis Top, Chassis Bottom
Length long side: 138mm
Cut angle: 22,5deg both sides
Units: 4 + 4
Assembly: Chassis Top, Chassis Bottom
Source model for all: “30x30 profile” / 30x30 profiles.FCStd
NOTE: In the 4 units for “Chassis Bottom” make an 8,2mm hole in the middle for caster wheels

## Slide 5
P0185 | Alu Profile L shape 15x15x1,5 106mm
Length long side: 206mm
Cut angle: 90deg
Units: 1+1
Assembly: Laser beam area – Bottom, Laser beam area – Top
Source Model: “Aluminum Profile L shape type 004” / Aluminum Profiles.FCStd

## Slide 6
P0190 | Alu Profile L shape 15x15x1,5 135mm 22,5 deg
Length long side: 135mm
Cut angle: 22,5deg both sides
Units: 2 + 2
Assembly: Laser beam area – Bottom, Laser beam area – Top
P0195 | Alu Profile L shape 15x15x1,5 137,5mm 22,5deg
Length long side: 137,5mm
Cut angle: 22,5deg both sides
Units: 2 + 2
Assembly: Laser beam area – Bottom, Laser beam area – Top
Source Model for all: “Aluminum Profile L shape type 002” / Aluminum Profiles.FCStd
NOTE: Install M5 threaded rivet as shown

## Slide 7
Length long side: 197mm
Cut angle: 90deg both sides
Units: 2
Assembly: Laser beam area – Top
P0200 | Alu Profile L shape 15x15x1,5 197mm
Source Model: “Aluminum Profile L shape type 003” / Aluminum Profiles.FCStd

## Slide 8
Length long side: 195mm
Cut angle: 22,5deg both sides
Units: 2
Assembly: Laser beam area – Bottom
P0205 | Aluminum Profile L shape 20x20x1,5 195mm 22,5 deg
Source Model: “Aluminum Profile L shape type 005” / Aluminum Profiles.FCStd

## Slide 9
P0215 | Alu Profile square 10x10x1 259mm with holes
Length long side: 259mm
Cut angle: 90deg both sides
Units: 2
Assembly: Chassis Middle
Source Model: “Z_Alu Profile square 10x10x1 with holes” / Aluminum Profiles.FCStd
NOTE: Install M5 threaded rivet as shown

## Slide 10
P0220 | Aluminum Profile L shape 30x20x1,5 250mm
Length long side: 250mm
Cut angle: 90deg both sides
Units: 2
Assembly: Batteries support
P0230 | Aluminum Profile L shape 30x20x1,5 98mm
Length long side: 98mm
Cut angle: 90deg both sides
Units: 2
Assembly: Batteries support
Source Model for all: “Aluminum Profile L shape type 001” / Aluminum Profiles.FCStd

## Slide 11
P0445 | DIN Rail 260mm
Length: 260mm
Cut angle: 90deg both sides
Units: 1
Assembly: Flexisoft set
NOTE: AGV_Soporte_motor_D (30mm diameter) overlaps 7mm

## Slide 12
P0325
P0325
P0340
P0350
P0350
P0355
P0355
P0375
P0375
P0380a
P0380b
P0380b

## Slide 13
P0345
P0345
P0370
P0370
P0360
P0360
P0365
P0365

## Slide 14
P0325 | Laser Support
Source: Plastic sheet 3mm
Units: 2
Assembly: Laser Set
Source Model: “Laser Supports” / Laser supports.FCStd

## Slide 15
P0340 | PVC 3mm piece: Top cover
Source Model: “Top cover” / AGV-Parts v4.FCStd
Source: Plastic sheet 3mm, 405x405mm
Color: Gray
Units: 1
Assembly: Top cover set

## Slide 16
P0345 | PVC 3mm piece: Front Side-Bottom Cover
Source Model: “Front Side-Bottom Cover” / AGV-Parts v4.FCStd
Source: Plastic sheet 3mm
Color: White
Units: 2
Assembly: Sides cover Set

## Slide 17
Source Model: “Front Side-Top Cover” / AGV-Parts v4.FCStd
P0370 | PVC 3mm piece: Front Side-Top Cover
Source: Plastic sheet 3mm
Color: White
Units: 2
Assembly: Sides cover Set

## Slide 18
Source Model: “Lateral-Top Cover” / AGV-Parts v4.FCStd
Source: Plastic sheet 3mm
Color: White
Units: 2
Assembly: Sides cover Set
P0360 | PVC 3mm piece: Lateral-Top Cover

## Slide 19
Source Model: “Lateral-Bottom Cover” / AGV-Parts v4.FCStd
Source: Plastic sheet 3mm
Color: White
Units: 2
Assembly: Sides cover Set
P0365 | PVC 3mm piece: Lateral-Bottom Cover

## Slide 20
Source Model: “Lateral-Back Cover” / AGV-Parts v4.FCStd
Source: Plastic sheet 3mm
Color: Gray
Units: 2
Assembly: Sides cover Set
P0350 | PVC 3mm piece: Lateral-Back Cover

## Slide 21
Source Model: “Back Side Cover” / AGV-Parts v4.FCStd
Source: Plastic sheet 3mm
Color: Gray
Units: 2
Assembly: Sides cover Set
P0355 | PVC 3mm piece: Back Side Cover

## Slide 22
Source Model: “laser beam area sheet” / AGV-Parts v4.FCStd
Source: Plastic sheet 3mm, 261 x 405 mm
Color: Gray
Units: 1 + 1
Assembly: Laser beam area – Bottom / Laser beam area – Top
P0375 | PVC 3mm piece: laser beam area sheet
Cut all this part
145,9mm

## Slide 23
Source Model: “Inside wall” / AGV-Parts v4.FCStd
Source: Plastic sheet 3mm
Color: Gray
Units: 1
Assembly: Sides cover Set
P0380 | PVC 3mm piece: Inside wall (Part 1)
NOTES:
Could be done in one long piece (530x60), or split in three:
-Central part (from piece 103x60mm)
-2 Side parts (from 2 pieces 212x60mm)

## Slide 24
Source Model: “Inside wall” / AGV-Parts v4.FCStd
P0380 | PVC 3mm piece: Inside wall (Part 2)
60mm
15mm
7,5mm
7,5mm
30mm

## Slide 25
P0410 | Bracket front laser
Source Model: “Bracket front laser” / AGV-Parts v4.FCStd
Source: Aluminum sheet 30x1,5mm
Units: 2 + 2
Assembly: Laser beam area – Bottom / Laser beam area – Top

## Slide 26
Source Model: “Drive support” / AGV-Parts v4.FCStd
Source: Aluminum sheet 20x118x1,5mm
Units: 2
Assembly: Drives set
P0415 | Drive support
Install 2 M5 threaded rivets as shown in the picture. Each piece has the rivet in a different hole.

## Slide 27
Source Model: “Aluminum Profile L shape type 006” / Aluminum Profiles.FCStd
Source: Aluminum sheet 30x1,5mm
Units: 2
Assembly: RFID Set
P0425 | Bracket RFID
NOTE: Install M4 threaded rivet as shown (note it is in different hole in each piece)

## Slide 28
Units: 1, Printer file: AGV_Soporte_motor_D_v1.gcode
Material: PLA, Color: Gray, Weight: 44g, Printing time: 2h 33m
Assembly: Motors+Encoders
Source Model: “AGV_Soporte_motor_D” / AGV_Soporte_motor_D_v1.FCStd
P0290 | AGV_Soporte_motor_D
P0295 | AGV_Soporte_motor_I
Units: 1, Printer file: AGV_Soporte_motor_I_v4.gcode
Material: PLA, Color: Gray, Weight: 44g, Printing time: 2h 33m
Assembly: Motors+Encoders
Source Model: “AGV_Soporte_motor_I” / AGV_Soporte_motor_I_v4.FCStd
P0300 | AGV_Rueda
Units: 2, Printer file: AGV_Rueda_v3.gcode
Material: PLA, Color: Gray, Weight: 44g, Printing time: 4h
Assembly: Motors+Encoders
Source Model: “AGV_Rueda” / AGV_Rueda_v3.FCStd
P0260 | Axel clamp
Units: 1 + 1, Printer file: Axel clamp x2.gcode (2 units at once)
Material: PLA, Color: Gray, Weight: 20g, Printing time: 1h 13m
Assembly: Balancing axel set, Clutch set
Source Model: “Axel clamp” / Axel clamp.FCStd

## Slide 29
Units: 1a & 1b, Printer file: 16mm axel corner clamp side a_b long.gcode (both in one)
Material: PLA, Color: Gray, Weight: 21g, Printing time: 1h 24m
Assembly: Balancing axel set
Source Model: “16mm axel corner clamp side a long” / AGV_Clamp_eje_bal_v3.FCStd
Source Model: “16mm axel corner clamp side b long” / AGV_Clamp_eje_bal_v3.FCStd
P0265 | Clutch-cam A
P0270 | Clutch-cam B
P0250 | 16mm axel corner clamp side a long
P0255 | 16mm axel corner clamp side b long
Units: 1A & 1B, Printer file: Clutch Cam A and B.gcode (both in one)
Material: PLA, Color: Gray, Weight: 32g, Printing time: 1h 48m
Assembly: Clutch set
Source Model: “Clutch-cam A” / Clutch Cam A and B.FCStd
Source Model: “Clutch-cam B” / Clutch Cam A and B.FCStd
Units: 1 & 1A & 1B, Printer file: Clutch axel clamps and cap.gcode (all in one)
Material: PLA, Color: Gray, Weight: 14g, Printing time: 56m
Assembly: Clutch set
Source Model: “Clutch axel clamp A” / Clutch axel clamps.FCStd
Source Model: “Clutch axel clamp B” / Clutch axel clamps.FCStd
Source Model: “Clutch axel cup” / Clutch axel cup.FCStd
P0275 | Clutch axel cap
P0280 | Clutch axel clamp A
P0285 | Clutch axel clamp B

## Slide 30
Units: 4 + 4, Printer file: 135deg bracket type 002 x8.gcode (x8 parts)
Material: PLA, Color: Gray, Weight: 63g, Printing time: 4h 18m
Assembly: Chassis Top, Chassis Bottom
Source Model: “135 degree bracket type 002” / 135 degree bracket.FCStd
Units: 4 + 4, Printer file: ﻿135deg_small_braket M6 3holes type 002 x8.gcode (x8 parts)
Material: PLA, Color: Gray, Weight: 60g, Printing time: 4h 5m
Assembly: Chassis Top, Chassis Bottom
Source Model: “135deg_small_braket M6 3holes ” / 135degree_small_braket v2.FCStd
Units: 4 + 2, Printer file: ﻿30x30 corner bracket type 002 x6.gcode (x6 parts)
Material: PLA, Color: Gray, Weight: 48g, Printing time: 3h 26m
Assembly: Chassis Middle, Set limit motors Top
Source Model: “﻿30x30 corner bracket type 002” / AGV-Parts v4.FCStd
P0011 | 135 degree bracket
P0016 | 135deg_small_braket M6 3holes
P0021 | 90 degree bracket
Units: 2 + 2, Printer file: ﻿﻿Bracket Front Laser type 002 x4.gcode (x4 parts)
Material: PLA, Color: Gray, Weight: 11g, Printing time: 45m
Assembly: Laser beam area – Bottom / Laser beam area – Top
Source Model: “﻿Bracket Front Laser type 002” / AGV-Parts v4.FCStd
P0411 | Bracket front laser

## Slide 31
Units: 1, Printer file: Back top Cover v2.gcode
Material: PLA, Color: White, Weight: 107g, Printing time: 6h 33m
Assembly: Back Cover Set
Source Model: “Back top Cover v2” / AGV-Parts v4.FCStd
Units: 1, Printer file: Back bottom Cover.gcode
Material: PLA, Color: White, Weight: 92g, Printing time: 5h 23m
Assembly: Back Cover Set
Source Model: “Back bottom Cover” / AGV-Parts v4.FCStd
Units: 2, Printer file: RPiBox.gcode
Material: PLA, Color: White, Weight: 49g, Printing time: 3h 12m
Assembly: Back Cover Set
Source Model: “RPiBox” / AGV-Parts v4.FCStd
P0315 | Back top Cover
P0320 | Back bottom Cover
P0316 | RPiBox

## Slide 32
Units: 1, Printer file: Front Top Cover.gcode
Material: PLA, Color: White, Weight: 94g, Printing time: 5h
Assembly: Front Cover Set
Source Model: “Front Top Cover” / AGV-Parts v4.FCStd
Units: 1, Printer file: Front Bottom Cover.gcode
Material: PLA, Color: White, Weight: 96g, Printing time: 4h 50m
Assembly: Front Cover Set
Source Model: “Front Bottom Cover” / AGV-Parts v4.FCStd
P0305 | Front Top Cover
P0310 | Front Bottom Cover